## Slide 1
10/15/2024
Wei Gao1
1 University of Denver

## Slide 2: About Me
Currently
Postdoctoral Research Fellow at the University of Denver, Denver, Colorado, USA. Past
Ph.D. at University of Denver, Denver, Colorado, USA, in 2023.
M.S. at University of Denver, Denver, Colorado, USA, in 2019.
B.S. Hebei University of Technology, Tianjin, China, in 2017.
Research Interest
Microgrid control Renewable energy Power system dynamics Power system stability
Power system economics and market Machine learning application in power system
2 /
31

## Slide 3: Research and Project
Distributed Energy Resources Manamegent System (DERMS)
Adaptive Power System Protection with Inverter-based Resources (IBRs) Deep Reinforcement Learning based power system dynamic control
HVDC Oscillation Damping DFIG Fault-Ride-Through (FRT) Frequency Regulation
3 /
31

## Slide 4: Distributed Energy Resources Management System (DERMS)
Why
CYME lacks of OPF module (depreciated) as a power commercial distribution system analysis software
Goal
Develop a distribution level OPF based strategy
Work with Eaton research laboratory to develop a DERMS module for CYME software
Difficulties
Unbalance and mixture of single-phase and three-phase (multi-phase) in distribution level Linearization of Original nonlinear and nonconvex OPF model in multi-phase system
General and comprehensive devices support by CYME (overhead-lines, transformer, PV, BESS, regulator, capacitor, etc.)
4 /
31

## Slide 5: Formulation of OPF model
Subject to
powerflow equations
line and transformer
constraints
bus voltage constraints
operational generation constraints
min ∑
t=Δt..T
(cg,tPinj,t +
∑ α(∣Vi,t∣ − ∣Vi ∣)2)
nom
i=1..N
5 /
31

## Slide 6: Constraints
Powerlow equations:
Line and transformer constraints:
Bus voltage constraints:
Operational generation constraints:
N
Pi,t = ∑ ∣Vi,t∣∣Vj,t∣(Gij cos θij,t + Bij sin θij,t) = Pgi,t − Pdi,t
j=1
N
Qi,t = ∑ ∣Vi,t∣∣Vj,t∣(Gij sin θij,t − Bij cos θij,t) = Qgi,t − Qdi,t
j=1
∣Sij,t∣ ≤ Sijmax
Vimin ≤ ∣Vi,t∣ ≤ Vimax
SOCBESS = SOCBESS + (ηcP BESS Δt −
k,t+1 k,t k,c,t
ηd
k,d,t
0 ≤ P P V ≤ P P V
k,t kt,max
0 ≤ P BESS ≤ P BESS
k,c,t k,c,max
0 ≤ P BESS ≤ P BESS
k,d,t k,d,max
P BESS
k
Δt)/EBESS
6 /
31

## Slide 7: Powerflow Equations
Branch-low model (BFM)
Nonlinear and nonconvex
Good for unbalanced distribution system to linearize (LinDistFlow model)
Single-phase LinDistFlow model Three-phase LinDistFlow model
Bus-injection model (BIM) (presented in the previous slide)
Nonlinear and nonconvex
Good for balanced three-phase
transmission system
Pij + pj = ∑ Pjk ∀j ∈ N +
k:j→k
Qij + qj = ∑ Qjk ∀j ∈ N +
k:j→k
wj = wi − 2rij Pij − 2xij Qij ∀j ∈ N +
Pij,ϕ + pj,ϕ =
∑ Pjk,ϕ ∀j ∈ N +
k:j→k
Qij,ϕ + qj,ϕ =
∑ Qjk,ϕ ∀j ∈> N +
k:j→k
wj = wi + MP ,ij Pij + MQ,ij Qij
MP ,ij =
−2r11
r21 +
r31 −
3x21
3x31
r12 − 3x12
−2r22
r32 + 3x32
r13 +
r23 −
3x13
3x23
−2r33
MQ,ij =
−2x11
x21 +
x31 −
3r21
3r31
x12 −
3r12
−2x22
x32 +
3r32
x13 +
x23 −
3r13
3r23
−2x33
7 /
31

## Slide 8: Implementation
A python package to parse general CYME model
A Pyomo (open-source optimization modeling language) based LinDistFlow model
A general mixed-integer (with battery storage) nonlinear solver mindtpy (combined with GLPK and IPOPT) Communication between CYME and LinDistFlow OPF module via message passing interface (MPI)
Case Study (in progress)
4-Node-YY-Bal_dss IEEE-13 Node
IEEE-34 Node IEEE-123 Node
IEEE-123 Node with DERs
IEEE-123 Node with DERs and BESSs Modified IEEE-123 Node from CYME
8 /
31

## Slide 9: Case Study - Modified IEEE-123 Node from CYME
System Structure
Mixture of single-phase and three-phase Unbalanced overhead lines
Regulators Capacitors PVs BESSs
Optimization Period
24 hours with 1 hour resolution
Online optimization with feedback from the real-time power system data
9 /
31

## Slide 10
Preliminary Results
No DERs

## Slide 11
Preliminary Results
No DERs

## Slide 12: Preliminary Results
50% DERs
100% DERs

## Slide 13: Adaptive Power System Protection with IBRs
Why
Existing protection relay settings are heavily relied on the time-domain based simulation and analysis (difficult and time-consuming)
Existing protection relay settings are not performant or working due to the decreasing inertia of the system with more inverter-based resources (IBRs), as well the uncertainty of the IBRs
Goal
Develop a protection relay setting framework with IBRs via DRL, especially for out-of-step and power swing conditions
Work with SEL to integrate the DRL based adaptive protection settings into the physical relay via hardware-in-the-loop (HIL) testing
Difficulties
Recognize out-of-step and power swing conditions for the system Integrate the DRL based settings into the physical relay
HIL testing using RTDS platform

## Slide 14: Out-of-Step and Power Swing Conditions
Stable power swing
Oscillations between generators are stable
System returns to new equilibrium point
A large disturbance to the system such as faults, leads to two results:
Out-of-step
Loss of synchronism between two or more generators Cascading outages and system blackouts
Existing Dual-blinder Protection
Impedance seen by relay in complex plane Rate of change of impedance
Moves slow during stable power swing Moves fast during out-of-step
Principle of the dual-blinder relay
Monitor the time of impedance trajectory crossing the two blinders Setting of the dual-blinder relay
Zone 5: resistance and reactance thresholds Zone 6: resistance and reactance thresholds Crossing time threshold
Source: Fischer, Normann et al. “Tutorial on Power Swing Blocking and Out-of-Step Tripping.” (2015)

## Slide 15: Implementation (in progress)
Power system simulation with synchronous generator and IBRs (PV and DFIG) in PSCAD/EMTDC
DRL algorithm in Python with parallel computing in Ray framework
HIL testing with RTDS platform

## Slide 16: Deep Reinforcement Learning based power system dynamic control
Why
Convertional control strategies usually require linearized model
Fixed control parameters limit performance for various operating conditions DRL based algorithms
Data-driven, model-free No linearization is required
Goal
Develop a general DRL based control framework and platform for power system dynamic control
Difficulties
Efficient training process Reliable action space
Efficient reward function design

## Slide 17: Reinforcement Learning and Meta Learning
Elements
Agent - RL algorithm
Environment - Physical or simulated power system
States - Important system variables (differential and algebraic)
Actions - Control actions (discrete or continuous)
Reward - Measure the performance of the agent
Policy - Function to generate action (linear or nonlinear such as neural network, i.e., DRL)
Goal
Design an effective reward function to find the optimal policy in maximizing the expected
cumulative rewards
Meta Learning
Enhance DRL’s capability even more by exposing to more diverse environments (tasks) Utilize the knowledge in one task to improve the performance in another task efficiently Safe and reliable action facing new environments (tasks)
Apply to new environments (tasks) with little adaptation process
Environment
Action
Policy Agent
Policy update
Learning algorithm
State
Reward

## Slide 18: Meta-DRL Framework and Platform [1]
Framework
Robustness of Training Process
Online Data Pipeline
Parallel Execution
Cluster Layer
Database
Layer
States
Actions
Uncertenties
Different power flows cases
Different faults
...
Power System Environment
Area1 Area2
Instance 1
Instance 2
Instance 3
MSO Algorithm
MES Framework
GSES Algorithm
Latent Variable
System params
Projection
RL Policy
States
Actions
NN Weights
Real Time Streaming
Real Time Operational Data
Past Operational Data
Security Guaranteed Online Adaption
0
5
10
20
25
30
15
Iteration
210
205
200
195
190
185
180
Reward

## Slide 19: HVDC-based oscillation damping control using Meta-DRL [4]
Problem
Inter-area oscillation threaten system stability
HVDC modulates power between two areas to damp oscillation
Conventional damping controller parameters are fixed and not
performant for various operating conditions and faults
Conventional damping control
Wide-area damping controller using PUM measurements Linearization of the system
Fixed controller parameters
DRL-based damping control
Adaptively regulate the reference signal of the exsiting controllers
Power
System
PMU
PMU
Filter
HVDC
PDC
ΔO(t)=∑ Ki× fi
PMU
…
...
ARS Control
Algorithm
V
ω
θ
θ
f | K1, K2, …,Kn | 

## Slide 20: Case Study 1 [4]
Revised minniWECC system with PDCI HVDC transmission
Two dominant modes
0.3 Hz Alberta mode
0.65 Hz BC mode

## Slide 21: Result of Revised minniWECC [4]
Loss of line (left), Single-phase fault (right)
(i) Results of Scenario I
(ii) Results of Scenario II
(i) Results of Scenario III
(ii) Results of Scenario IV

## Slide 22: Case Study 2 [1]
Modified IEEE-39 bus system with HVDC
2
30
1
39
9
8
4
14
3
25
37
26
28
29
27
15
16
17
5
6
7
18
12
13
11
31
10
32
24
21
22
38
35
36
23
19
20
34
33
HVDC
G1
G10
G2
G3
G4
G5
G6
G7
G8
G9

## Slide 23: Result of Modified IEEE-39 bus system with HVDC [1]
Training example of the system dynamics
Adaptation example of the system dynamics
Reward of MES over GSES in percent
0
20
2
1
0
100 MW
No_Ctrl GSES
5 10 15
(a) HVDC Line Flow (16 - 19)
MES
0
20
5 10 15
(b) Bus Frequency Difference (19 - 16)
0.0002
0.0000
0.0002
Hz
No_Ctrl
GSES
MES
0
20
5 10 15
(c) Machine Speed Difference (G3 - G5)
0.0010
0.0005
0.0000
0.0005
0.0010
p.u.
No_Ctrl
GSES
MES
0
5
20
10 15
Seconds
(d) Machine Angle Difference (G3 - G5)
0.40
0.45
0.50
0.55
0.60
Rad
No_Ctrl
GSES
MES
0.0
2.5
(a) HVDC Line Flow (16 - 19)
0.5
0.0
0.5
1.0
100 MW
No_Ctrl GSES
5.0 7.5
MES_No_Adapt MES_With_Adapt
10.0 12.5 15.0
2.5 5.0 7.5 10.0 12.5 15.0
(b) Bus Frequency Difference (19 - 16)
0.00010
0.0
0.00005
0.00000
0.00005
0.00010
Hz
0.0
2.5 5.0 7.5 10.0 12.5 15.0
(c) Machine Speed Difference (G8 - G5)
0.0005
0.0000
0.0005
p.u.
2.5
5.0 7.5 10.0 12.5 15.0
Seconds
(d) Machine Angle Difference (G8 - G5)
0.35
0.0
0.40
0.45
Rad
10.0%
0.0% 10.0% 20.0% 30.0%
Reward of MES over GSES in percentage
0
10
20
30
40
Count

## Slide 24: DFIG-FRT using DRL [5]
Problem
DFIG generates maximum power using MPPT during normal operation
DFIG rotor over-current and DC-link over-voltage due to terminal voltage dip during faults
Conventional FRT
Additional hardware (e.g., crowbar)
Rely on accurate mathematical model of the system
DRL-based FRT
Adaptively regulate the reference signal of the DFIG active power and DC-link voltage Smooth transition to new steady-state

## Slide 25: Case Study [5]
Grid-following-based DFIG
Active power/rotating speed
DC-link voltage and grid reactive power
DFIG
Grid
Fault
DFIG-Grid Transformer
Load
Transmission Line
Gear Box
DFIG
Grid
RSC
DC-link
m
P
isabc
Ps Qs
g
P
g
Q
igabc
rabc
i
P
r
Qr
vdc
vsabc
vrabc
GSC gabc
v
Pe Qe
Pitch control
s
P
t

DFIG Rotor-side Converter
Inner current loop
Rotor dq-axis currents ird and irq
Outer power loop
DFIG
Grid
RSC
DC-link
vdc
dq abc
Stator Flux
sabc
v
sabc
i

dq abc
Lrf Rrf
P*
+ e
PI
i*
+ rq
rq
i
-
PI
rq
v
6-channel
signal
PWM
PI
PI
e
+ Q*
-
Pe
Qe
-
rd
ird
- + i*
vrd
dq
abc
r
-
+  s Calculation
t
MPPT
Rated
Power
Calculation
rabc
v*
rabc
i
DFIG Grid-side Converter
Inner current loop
Grid dq-axis currents igd and igq
Outer power loop
Grid
GSC
DC-link
vdc
dq abc
Power
Calculation
PLL
Rgf Lgf
Cgf
gabc
v
gabc
i
g

vdc
-
*
+ vdc
PI
*
i
gd
i
-
PI
6-channel
signal
PWM
PI
PI
g
+ Q*
Qg
-
+ gq
i*
+ gd
gq
i
-
gq
v
vgd
dq
abc
rabc
v*
Grid-side
Transformer
gabc
dq abc
i

## Slide 26: Result of DFIG-FRT [5]
Three-phase fault with 50% voltage drop

## Slide 27: Result of DFIG-FRT [5]
Three-phase fault with 100% voltage drop

## Slide 28: Result of DFIG-FRT [5]
Metallic single-line-to-ground fault

## Slide 29: Frequency Regulation using DRL [2, 3]
Problem
Frequency regulation is done by synchronous generators (SG) due to the natural inertia Low system inertia due to the increasing penetration of inverter-based resources (IBRs)
Conventional frequency regulation
Additional battery energy storage system (BESS)
Pitch control of wind turbines system to regulate the power output and maintain the system frequency
DRL-based frequency regulation
Adaptively adjust the reference signal of the exisiting pitch angle controller Stabilize system frequency during events
Avoid unnecessary load shedding

## Slide 30: Case Study [2, 3]
One SG replaced by DFIG in a modified IEEE-39 bus system
Loss of generator
Sudden increase of load
Sudden decrease of load

DFIG
RSC
GSC
DC-link
m
P
vdc
vrabc
vsabc Pe Qe
Main
Grid
Pitch
control
Ps
t
Gear
Box
RL
control

## Slide 31: Publications
Gao, W., Fan, R., Huang, Q., & Gao, W. (2024). A Meta-Strategy Approach to Inter-Area Oscillation Control. IEEE Transactions on Power Systems. (Submitted)
Gao, W., Fan, R., Qiao, W., Wang, S., & Gao, W. (2023). Deep Reinforcement Learning Based Control of Wind Turbines for Fast Frequency Response. IEEE Industry Applications Society (IAS) Transactions. (Submitted)
W. Gao, R. Fan, W. Qiao, S. Wang and D. W. Gao, "Fast Frequency Response Using Reinforcement Learning-Controlled Wind Turbines," 2023 IEEE Industry Applications Society Annual Meeting (IAS), Nashville, TN, USA, 2023, pp. 1-7, doi: 10.1109/IAS54024.2023.10406378.
Gao, W., Fan, R., Huang, R., Huang, Q., Gao, W., & Du, L. (2023). Augmented random search based inter-area oscillation damping using high voltage DC transmission. Electric Power Systems Research, 216, 109063.
Gao, W., Fan, R., Huang, R., Huang, Q., Du, Y., Qiao, W., … & Gao, D. W. (2022). Improving DFIG performance under fault scenarios through evolutionary reinforcement learning based control. IET Generation, Transmission & Distribution.
Gao, W. (2021, April). PV Array Fault Detection Based on Deep Neural Network. In 2021 IEEE Green Technologies Conference (GreenTech) (pp. 42-47). IEEE.
Gao, W. (2020, July). Microgrid control strategy based on battery energy storage system-virtual synchronous generator (BESS-VSG). In 2020 IEEE Kansas Power and Energy Conference (KPEC) (pp. 1-6). IEEE.
Huang, R., Gao, W., Fan, R., & Huang, Q. (2022). Damping inter-area oscillation using reinforcement learning controlled TCSC. IET Generation, Transmission & Distribution.
Huang, R., Gao, W., Fan, R., & Huang, Q. (2022). A Guided Evolutionary Strategy Based Static Var Compensator Control Approach for Inter-area Oscillation Damping. IEEE Transactions on Industrial Informatics.
Li, Y., Gao, W., Huang, S., Wang, R., Yan, W., Gevorgian, V., & Gao, D. W. (2021). Data-driven optimal control strategy for virtual synchronous generator via deep reinforcement learning approach. Journal of Modern Power Systems and Clean Energy, 9(4), 919-929.
Q. Li, L. Cheng, W. Gao, and D. W. Gao, “Fully distributed state estimation for power system with information propagation algorithm,” Journal of Modern Power Systems and Clean Energy, vol. 8, no. 4, pp. 627–635, 2020.
Y. Li, D. W. Gao, W. Gao, H. Zhang, and J. Zhou, “Double-mode energy management for multi-energy system via distributed dynamic event-triggered newton- raphson algorithm,” IEEE Transactions on Smart Grid, vol. 11, no. 6, pp. 5339– 5356, 2020.
T. Gao, W. Gao, J. J. Zhang, and W. D. Gao, “Small-scale microgrid energy market based on pilt-dao,” in 2019 North American Power Symposium (NAPS), IEEE, 2019, pp. 1–6.
W. Yan, X. Wang, W. Gao, and V. Gevorgian, “Electro-mechanical modeling of wind turbine and energy storage systems with enhanced inertial response,” Journal of Modern Power Systems and Clean Energy, vol. 8, no. 5, pp. 820–830, 2020.
L. Yu-Shuai, L. Tian-Yi, G. Wei, and G. Wen-Zhong, “Distributed collaborative optimization operation approach for integrated energy system based on asynchronous and dynamic event-triggering communication strategy,” Acta Automatica Sinica, vol. 46, no. 9, pp. 1831– 1843, 2020.
Y. Li, D. W. Gao, W. Gao, H. Zhang, and J. Zhou, “A distributed double-newton de- scent algorithm for cooperative energy management of multiple energy bodies in energy internet,” IEEE Transactions on Industrial Informatics, vol. 17, no. 9, pp. 5993–6003, 2020.
W. Yan, W. Gao, D. W. Gao, and J. Momoh, “Stability-oriented optimization and consensus control for inverter-based microgrid,” in 2018 North American Power Symposium (NAPS), IEEE, 2018, pp. 1–6.
X. Guan, W. Gao, H. Peng, N. Shu, and D. W. Gao, “Image-based incipient fault classification of electrical substation equipment by transfer learning of deep convolutional neural network,” IEEE Canadian Journal of Electrical and Computer Engineering, vol. 45, no. 1, pp. 1–8, 2021.
K. Yang, W. Gao, and R. Fan, “Optimal power flow estimation using one-dimensional convolutional neural network,” in 2021 North American Power Symposium (NAPS), IEEE, 2021, pp. 1–6.
K. Yang, W. Gao, R. Fan, T. Yin, and J. Lian, “Synthetic high impedance fault data through deep convolutional generated adversarial network,” in 2021 IEEE Green Technologies Conference (GreenTech), IEEE, 2021, pp. 339–343.
X. Xiangyu, S. Xue, H. Peng, N. Shu, W. Gao, and D. W. Gao, “Contact failure diagnosis for gis plug-in connector by magnetic field measurements and deep neural network classifiers diagnostic des d ́efauts de contact du connecteursig bas é sur la mesure du champ magn ́etique et le classificateur du r ́eseau neuronal profond,” IEEE Canadian Journal of Electrical and Computer Engineering, 2022.
W. Yan, W. Gao, T. Gao, D. W. Gao, S. Yan, and J. Wang, “Distributed cooperative control of virtual synchronous generator based microgrid,” in 2017 IEEE International Conference on Electro Information Technology (EIT), IEEE, 2017, pp. 506–511.
Y. Shen, W. Gao, D. W. Gao, and W. Yan, “Inverter controller design based on model predictive control in microgrid,” in 2017 IEEE International Conference on Electro Information Technology (EIT), IEEE, 2017, pp. 436–441.
W. Chen, J. Wang, W. Gao, D. W. Gao, B. Wang, and H. Wang, “Power optimization control of doubly fed induction generator based on active power reserve,” in 2016 North American Power Symposium (NAPS), IEEE, 2016, pp. 1–6.
V. Gevorgian et al., “Wgrid-49 gmlc project report: Understanding the role of short- term energy storage and large motor loads for active power controls by wind power,” National Renewable Energy Lab.(NREL), Golden, CO (United States), Tech. Rep., 2019.
W. Yan, L. Cheng, S. Yan, W. Gao, and D. W. Gao, “Enabling and evaluation of inertial control for pmsg-wtg using synchronverter with multiple virtual rotating masses in microgrid,” IEEE Transactions on Sustainable Energy, vol. 11, no. 2, pp. 1078–1088, 2019.
W. Yan, W. Gao, W. Gao, and V. Gevorgian, “Implementing inertial control for pmsg-wtg in region 2 using virtual synchronous generator with multiple virtual rotating masses,” in 2019 IEEE Power & Energy Society General Meeting (PESGM), IEEE, 2019, pp. 1–5.
X. Wang et al., “Implementations and evaluations of wind turbine inertial controls with fast and digital real-time simulations,” IEEE Transactions on Energy Conversion, vol. 33, no. 4, pp. 1805–1814, 2018.
X. Guan et al., “Deterioration behavior analysis and lstm-based failure prediction of gib electrical contact inside various insulation gases,” IEEE Access, vol. 8, pp. 152 367–152 376, 2020.
Y. Huang, Q. Sun, Y. Li, W. Gao, and D. W. Gao, “A multi-rate dynamic energy flow analysis method for integrated electricity-gas-heat system with different time-scale,” IEEE Transactions on Power Delivery, 2022.
Wei Gao Research Topics
31 / 31